## Slide 1
Next Gen Open Source Flexible
Engine Management

## Slide 2: What is rusEFI?
Project started 2013
First hardware developed Q4 2013
4 current boards
~100,000 lines of C++
Around 20 active developers
~ 45 different engines running so far
Goals -
Flexible open source engine control

## Slide 3: Features
C++ open source software featuring:
TunerStudio integration for online tuning
16x16 fuel, VE, timing tables
Spark control: distributor, wasted & sequential options
Fuel Injection: single, batch & sequential options
Closed loop idle control - solenoid or stepper
Basic CAN integration
Basic GPS integration
High speed data logging up to 150hz
Individual cylinder ignition trim
FSIO for special custom functions
Hardware features:
ARM 32 bit processor – STMF767 215mhz or STMF407 168mhz
Flexible hardware – Adaptable, Expandable, Reparable, and most conventional parts usable
Up to 12 cylinders

## Slide 4: Upcoming features
Near future:
Knock sensing
Onboard wideband feedback
VVT
Front end for FSIO programing
Direct injection
MAF based fuelling
Fail safe ETB
Long term goals:
Simulink/Scilab integration for strategies
Modular hardware for development or research

## Slide 5: Early Boards
Frankenstein Released 2013 First Development board
Replaced by Frankenso
Frankenso Released ???? Current development board Designed as direct fit for Denso OEM applications
Still in use for development

## Slide 6: Current Boards
Prometheus – A drop in replacement for the SECU-3i
4 cylinder only

## Slide 7: Current Boards
Micro rusEFI (MRE) – Miniature unit for space limited applications
Intended for 4 cylinder port injected engines
Can use all the software features of the full size units

## Slide 8: Current Boards
Proteus - A high-featured board for more complex engines (due late 2019)
16x 4A Low side drivers – injectors
12x 5v High/Low drivers - ignition
Dual ETB
4x 12v High side drivers – solenoids
10-pin internal header for knock expansion board